## Slide 1: Character Recognition for Degraded Engraved Text
Team 14
Mohd. Akram Memon
Ronak Totla
K.J.Somaiya College Of Engineering, Mumbai

## Slide 2: Introduction
Labourers with poor literacy: difficult to read the code
Human entry errors: missing, duplicate, incorrect sequence
UID codes are noted on challans: illegible for data entry operator
Less accessibility: closely packed array of cylinders
Warehouses: poorly illuminated areas
High probability : Data entry operator receives wrong UID codes
& hence, enters faulty data in cylinder inventory software
Problems:-
Error in cylinder tracking and maintenance
Safety regulations: hydro-test and explosive test after specified period of time. Wrong entry-> Cylinder can’t be tracked, this may cause hazardous consequences.
Cylinders are used on rent basis. Wrong data results in error in rent calculation.
Some cylinders are lost in this process and the owner has to bear the losses

## Slide 3: Problem Statement
The project addresses the issue of reduction in the rent losses (as well as product losses) by improving the efficiency of inventory management and tracking system.
Aims at providing an ease for all the steps involved
Friendly GUI, Database testing, Correction, etc.
Developing the semi-autonomous system to be compatible with the existing system

## Slide 4: Task Specifications
Image thresholding, particle filter
White text on black background detection and vice versa
Calculating character tilt dynamically
Dynamic ROI Calculation and Image segmentation
Character set training and OCR
Wireless communication range 80-100m
Database reading
Most probable database-lookup correction
Camera interfacing (wired and wireless) drivers
Hardware UART, Zigbee, LCD coding

## Slide 5: Project Plan
Phase I : Learning of LabVIEW and hardware
Phase II : Implementing the system with wireless camera
Phase III : Implementing the system with wired camera
Phase IV : Final GUI, small but important changes in the system

## Slide 6: Workflow of the system
Start
Initial configuration
Placing the camera and switch on device
Image is processed and signaling done
Database related process
Finish and next
If
signaling
reqd.?
Yes
No
Appropriate message to user

## Slide 7: Workflow of the system (cotd.)
Initial configuration: VI starts,selecting COM port, camera be configured, set up baud rate, optional manual crop, etc.
Placing the camera and switching the device on
Captured image is processed and appropriate signalling is shown to the manual operator to capture next image
Database related processes are completed
Signalling to the user if necessary
Go to step 2

## Slide 8: Innovations and challenges
Shifting from Matlab to LabVIEW after developing few codes
Writing camera drivers which are not supported on Windows 7
Pixel to length (cm) calibrations
Removing external illumination and providing diffused illumination
Dynamic ROI calculation
Dynamic tilt calculation

## Slide 9: Tasks completed
Camera interfacing
Problem : Both cameras not compatible with windows 7
Solution : Wireless camera  Using “exescript”, screenshot and crop
Wired camera  Creating our own drivers “*.dll”
Tilted images
Problem : Image with more than 6 degrees of tilt gives faulty o/p
Solution : Calculating the centroids of bounded box and hence getting the degree of tilt

## Slide 10: Tasks completed (cotd.)
Debugging of the code
Problem : Many difficulties during debugging/editing of code
Solution : Implementation of standard state machines and modular development of the code
Database correction
Problem : Image processing is not 100% accurate
Solution : Results after processing are matched with the database to get/predict the correct string

## Slide 11: Test review
Test criteria : Particle filter
Test description : Use of NI Vision Assistant module to specify the pixel size of the particles to be removed
Performance : Bounded areas with size less than the specified (9mm) were removed
Test criteria : Black on white/White on black recognition
Test description : Horizontal profile taken to get the mean. This mean is compared with the threshold (127) to decide the background color
Performance : Estimation of background and character color is hence done

## Slide 12: Test review (cotd.)
Test criteria : ROI calculation
Test description : Transitions in the intensities of mean vertical profile are plotted for dynamic ROI calculation
Performance : ROI based segmentation gave out fruitful results thus ensuring that the algorithm was correct
Test criteria : Database predictions
Test description : Matrix format of the entries from the database are compared (by correlation) from the matrix formats of the recognized string
Performance : Misread entries were predicted correctly

## Slide 13: Re-usability factors
For modular programming project is divided into four modules :
Image capturing
Image processing
OCR unit
Database interfacing
Development of the codes as per standards like implementing standard state machines, separate Vis for small functions, documentation of code in the code itself, etc.
Debugging indicators implemented which helps in tracing the error root and the type

## Slide 14: Future scope
Viewing it as a product:
Considering the system as a finished product, it is vital that the system be robust. Hence shaping it considering the same aspects of a finished product is necessary.
Image processing:
More robust image processing algorithms for recognition
Character connection and prediction codes dedicated for engraved targets

## Slide 15: Future scope (cotd.)
Additional features
Barcode reading, reading multiple words separated vertically, etc.
Hardware module
Permanent low cost hardware module with camera casing mounted
Adaptability
System should adaptable to many and all conditions

## Slide 16: Thank you !!!